## Slide 1: UVM Verification of ALU Design
Submitted by:
Fagr Ahmed Abd Elrazek “AUC section 12” ID:V23010586
Marwa Moaz “AUC section 14” ID:V23009897
Mohamed Yasser “AUC section 16” ID:V23010495
shurooq Mohammad Hassan Alshal “AUC section 12” ID:V23010529
Submitted to:
Dr. Ahmed Saeed
Eng. Randa Aboudeif

## Slide 2: Agenda
Introduction
Verification Environment
TLM
Scoreboard
Coverage and Randomization
Commands used

## Slide 3: Introduction

## Slide 4: Introduction
UVM verification of ALU design
ALU performs different arithmetic & logic operations in addition to NOP
THE UVM environment consists of 1 active agent agent and 1 environment class
The input carries and opcode are randomized
Code Coverage and functional coverage are collected
The scoreboard contains the reference model
Coverage percent is 100% and no errors are detected from the scoreboard

## Slide 5: Verification environment

## Slide 6: Environment

## Slide 7: TLM

## Slide 8: TLM
Analysis port at the Monitor
Analysis export at the agent
Analysis imp at the Scoreboard
Analysis imp at the Coverage
Connection in Environment

## Slide 9: Scoreboard

## Slide 10: Scoreboard
Implements reference model to mimic the ALU performance
Compare the dut output with scoreboard output and evaluate the number of errors
No errors are present

## Slide 11: Coverage and Randomization

## Slide 12: Coverage &Randomization
Randomize opcode and inout carries
Coverage on carries and opcode
Achieve 100% code and functional coverage

## Slide 14: Commands used

## Slide 15: Commands used
VCS:
Compilation
vcs – sverilog -ntb_opts uvm-1.2 testbench.sv
Simulation
./simv simv.log +UVM_TESTNAME=alu_base_test
Coverage
./simv -cm line+cond+fsm -cm_name testbench
urg -dir ./simv.vdb -format both